## Slide 1: Search Strategies for Topological Network Optimization
Abin Joseph: CB.EN.P2AIE22012

## Slide 2: Introduction
We consider an application of combinatorial search to the optimization of topologies in series-parallel networks
We propose a recursive search over the space of decomposition trees, in which partial solutions are obtained by exploring k-way partitionings of expandable nodes
Finally, we evaluate our approach on a parameterized benchmark suite of electrical circuits, demon- strating over an order of magnitude improvement in perfor- mance as compared to a baseline implementation

## Slide 3: Introduction
There exists a deep and widely-understood relationship be- tween the subjects of combinatorial optimization and net- work theory
Their affinity is perhaps best exemplified by constraint networks , in which the values of a finite set of variables interact by way of connections that restrict their mutual assign- ments
De- spite subtle differences in how constraints and domains are modeled, all these formulations share a common trait: the network serves as a static specification, its contents used by search as a roadmap when exploring the space of solutions
Our approach embraces the principles of advanced combinato- rial search, where optimal solutions can be obtained without resorting to brute-force enumeration

## Slide 4: Background
The focus of this work lies at the intersection of multiple specialties, including graph theory, electronic design automation, network optimization, and combinatorial search
Indeed, our approach builds upon a wealth of previous contributions to these areas, which we briefly cover in the following sections

## Slide 5: Graph Theory
A network is said to be series-parallel if it can be reduced to a single edge through repeated contraction, whereby any degree-2 node is replaced by an edge, and any parallel edges sharing common endpoints are collapsed into one
To the best of our knowledge, the study of series-parallel networks as a serious topic for discrete mathematics was first proposed in the late 19th century, motivated by the immense variety of configu- rations observed in electrical circuits
The relationships between series-parallel topologies and conflu- ent networks & combinatorial pregeometries were explored in two other seminal works

## Slide 6: Electronic Design Automation
The topic of optimization is front-and-center in modern electronics
The computer- aided design of integrated circuits is traditionally broken down into two categories: the former deals with logical synthesis , such as technology mapping and equivalence verification
With modern designs containing billions of transistors, the optimization strategies for these “mega-networks” are limited to the realm of suboptimal search

## Slide 7: Network Optimization
Outside the context of circuits, network optimization is a widely-celebrated topic that spans many areas
Real-world applications of network design are numerous, extending to the optimization of transportation costs , communication networks , reliable sys- tems , supply chains , wireless networks , transmission pipelines , water distribution networks , and photo- voltaic systems
Several of these employ the same class of series-parallel networks that inter- est us, yet their methodologies are limited to local search due to computational intractability

## Slide 8: Combinatorial Search

## Slide 9: Problem Definition
In other words, the network optimization problem is defined as a set of numeric labels, where the goal is to find the optimal series-parallel network made from the elements in the set, using monotone operators for series and parallel connections.
The cost of the network is defined as the difference between the value of the network and the target network value.
The objective is to minimize this cost by finding the series-parallel network that is closest to the target value

## Slide 10: Application to Electrical Circuits
The problem of combining raw components to achieve a desired total resistance is relevant in electrical circuits.
The total resistance of resistors in series is additive, and for resistors in parallel, it is reciprocal.
The values of the raw components are predetermined and standardized for inventory simplification.
A 7-resistor example is given with a target resistance of √7.
One solution to this problem involves three series connections whose combined resistance equals 90/29 Ω with a difference of 0.4577 from the target resistance.

## Slide 11: Sensitivity to Solution Structure
The first challenge relates to the sensitivity of the objective function to small changes in solution structure
Number par- titioning has been shown to exhibit weakest-link optimality , a property that allows the construction of globally optimal complete solutions from locally suboptimal partial solutions
Modern implementations exploit this by re- laxing upper and lower bounds on solution quality during re- cursive decomposition

## Slide 12: Similarities to Number Partitioning
Any partitioning of resistors can be translated into a valid series-parallel circuit, and so our formulation bears some re- semblance to the number partitioning problem , which seeks to divide a set of n elements across k partitions S1, S2, ..., Sk so as to minimize the maximum subset sum
Our partitioning turns out to be an optimal so- lution for the case where k = 3, since the maximum subset sum of 10 cannot be reduced
tential to require more computational effort when exploring the space of solutions

## Slide 13: Size of Solution Space
The difficulty described in the previous section is com- pounded by a second major challenge: the solution space of viable network topologies is overwhelmingly large
Since the presence of branch- ing subcircuits provides an increase in topological flexibility, high-quality solutions tend to make liberal use of them
In- deed, our circuit in Figure 3 is optimal; we leave it as an exercise to the reader to verify that its total resistance is 127/48 Ω, a value that lies remarkably close to our target: In Table 1, we compare the number of partitionings over n labels to the number of series-parallel networks containing n elements.1

## Slide 14: Our Approach
In this section, we outline our basic approach to the topo- logical optimization of series-parallel networks
It can be characterized as exact , anytime , and fast

## Slide 15: Solution Representation
To encode solutions, we make use of decomposition trees , a recur- sive structure that represents series and parallel connections as alternating layers of intermediate nodes
They are also cosmetically comparable to the AND/OR trees prevalent in optimization for graphical mod- els , with the obvious exception that we use them to cap- ture network topologies rather than search spaces
The decomposition tree for our optimal solution presented earlier is shown in Figure 4, using squares and circles to indi- cate series and parallel connections, respectively

## Slide 16: Recursive Decomposition
Select an expandable node S0 from a decomposition tree T.
Explore all possible k-way partitioning (k > 1) of S0 over its elements.
Expand the resulting decomposition tree T0 for each partitioning until no expandable nodes remain.
The leaf nodes represent complete solutions, and the approach performs a recursive search over nodes that represent recursive decompositions of the network elements.

## Slide 17: Bounding Conditions
The number of decomposition trees for topological optimization of series-parallel networks is prohibitively large, making an exhaustive search impractical.
Partial solutions can be pruned by utilizing the monotonicity of network operators through branch-and-bound pruning and the convexity of the objective function through tabulation and accelerated retrieval.
Lower bounds on the value of a partial solution can be obtained by applying monotone operators to the elements of each expandable node.
If the lower bound is sufficiently large, the partial solution can be abandoned.

## Slide 18: Exploiting Convexity with Tabulation
During the exploration of decomposition trees, it is in- evitable that many subsets of network elements will be en- countered at multiple expandable nodes
In this section, we reveal two techniques that can significantly help to avoid re- dundant recomputation of such subproblems

## Slide 19: Case #1: Singleton Expandables
Consider the two partial solutions in Tree, both of which contain a solitary expandable node
In each tree, the subset tree: Exploiting convexity via binary search for singleton expandables, or dual linear sweep for expandable pairs

## Slide 20: Case #2: Expandable Pairs
In this case, when there are only two expandable nodes S0 and S1, the solution space becomes more complex. To address this challenge, the authors leverage the concept of convexity. The idea is to begin with the lower and upper bounds, respectively, and then perform a dual linear sweep over the space of pairwise configurations.

## Slide 21: Case #2: Expandable Pairs
Compare the resulting network with the target value. If the value of network is smaller than target value, the authors consider a subcircuit for S0 with the next higher value in the lookup table. On the other hand, if network is greater than target value, they consider a new subcircuit for S1, taking the next lower value.

## Slide 22: Case #2: Expandable Pairs
This approach reduces the number of candidate solutions, as it navigates a narrow corridor of potentially cost-minimizing networks. This technique is inspired by a landmark improvement to algorithms for the knapsack problem

## Slide 23: Empirical Results
To evaluate the efficiency of our algorithm, we introduce a benchmark suite containing parameterized electrical circuits of increasing difficulty
For progressively larger values of n, we assign S and fT as follows: 10: else if 2 = ∅ and max then

## Slide 24: The Complete Algorithm
If no expandable node remains, the solution is complete, and is stored along with its associated cost
If exactly one expandable node remains , we perform a binary search over precomputed subcircuits to retrieve its replacement
If exactly two expandable nodes remain , we perform a dual linear sweep over precomputed subcircuits to retrieve their replacements
For any other partial solution, we select a node to expand and iterate over its viable partitioning

## Slide 25: The Complete Algorithm
An exhaustively enumerative baseline
A branch-and-bound version that uses fL and
A version that exploits convexity with tabulation
Finally, a version that combines all techniques described in this paper

## Slide 26: Special Cases
While our problem statement is crafted to be broadly applicable, certain special cases are more likely to be encountered in practice than others
Here, we cover two such variations, and discuss strategies to ensure efficient performance

## Slide 27: Optional Exclusion of Network Elements
Any 0-Ω resistor should be placed at most one level deep
Any 0-Ω subcircuit should be at most one element wide

## Slide 28: Duplication of Network Elements
Our choice of multiset foris delib- erate; given sufficient inventory, there may be many copies of the same network element available for use
Since dupli- cates are interchangeable, their presence affords additional opportunities for runtime reduction via symmetry breaking
By incorporating this adaptation, we were able to produce the 15-element circuit in Figure 9 com- prised entirely of 1-Ω resistors that approximates π to six digits: Figure 8: The optimal solution for n =

## Slide 29: Future Work
We believe that the study of topological network optimization will continue to be an attractive area for future work
One possible avenue of research is to broaden the application of tabulation to the case of three or more expandable nodes

## Slide 30: Future Work
The optimization of series-parallel networks presents a challenging problem that requires the development of efficient and effective algorithms. Our work provides a promising foundation for future research in this area, by introducing novel techniques for reducing the search space and improving the efficiency of network optimization algorithms. There are many interesting directions for future work, such as exploring alternative search strategies, broadening the application of tabulation, and investigating the optimization of other types of networks. The ultimate goal is to design fast and efficient algorithms that can produce high-quality solutions to the topological optimization of series-parallel networks.

## Slide 31: Conclusion
In conclusion, this work presents a novel approach to optimizing series-parallel networks that leverages a combination of search strategies, including branch-and-bound pruning, tabulation, and accelerated retrieval. The performance of our algorithm has been demonstrated through a new suite of parameterized benchmarks, and has shown to significantly reduce the computational burden of constructing optimal solutions. The domain agnostic nature of our approach allows for its application to the design of any network that meets the criteria of our formulation.